## Slide 1: Implementing the SRAM controller into sp6fmt
Riccardo T., Davide F.
(updated on 27 August 2013)

## Slide 2
Goals:
Implement SRAM functionality on sp6fmt
Operate with 100 MHz clock frequency
Source firmware available in
  atlasgroups/Detectors/Pixel
  IBLdev/RODcode/trunk/ROD_firmware/revC/spartan6/sp6fmt_ssram_100_28aug/sp6fmt

## Slide 3: Sp6fmt histogrammer
Svn revision : 10585
Use internal BRAM as memory
Dowloaded before updates announced by Moritz (see 3rd of July meeting)
Memory data bus 32-bit width
Histogrammer and BRAM have the same clock (100 MHz)
BRAM true dual port :
read and write accesses could be simultaneous
not arbitrated by the fw

## Slide 4: Histo unit layout
Addr_converter
Histo Top
DMA FIFO
EFB
valid
row
col
chip
tot
Rfd
(ready
For data)
enable
Pix Addr
Tot_val
histo
valid
Roc
(read-out
completed)
To
Micro
blaze
mode
rfr

## Slide 5: Hito unit – config & parameter
Control(1:1) = 0 (=occupancy mode) , 1 (tot mode)
Control(0:0) = 0 (= 1-chip), 1 (all 8 chips)
Control(3:2) = 3 (= full row)
2 (= 1/2 row)
      1 (= 1/4 row)
      0 (= 1/8 row)
Chip_size = row (336) * col (80)
#of_chip = 23 (1 in simulation)
MaxAddr = Chip_size * #of_chip

## Slide 6: Histo – controller state machine
RESET
INIT
SAMPLE
READOUT
PREPARE
CLEAN
IDLE
Select ScanType
Select ReadOut mode
HiAddr <= controlReg
localAdd= MaxAddr
mode
RamValidPipe
mode
localAdd=HighAddr
ramCleanAdd
=HighAddr
mode
Async rst
T
F
T
T
F
F
1
1
1
1
0
0
0
0

## Slide 7: Histo – layout (1/4) enables and address
Sample
Init
Readout
Clean
others
ramWrHisto
1
0
Sample
Readout
others
enable
rfr
0
ramRd
ramClean
WE
RE
R_ack
Sample
Readout
others
0
ramValidPipe
ramValidPipe1
FifoHistoPipe(0)
(valid)
Sample
others
LocalAdd
PixAddr
Sample
Readout
Clean
others
LocalAdd
HISTO UNIT
RAM
WrAddr
RdAddr
writeAddrHisto
ramCleanAddr

## Slide 8
HISTO UNIT
RAM
Histo – layout (2/4) data
tot
Tot_val
*
+
+
+
1
Sample
others
0
ramDatainHisto
WrData
RdData
ramDataOut
ramDataOutPipe
fifoHistoPipe1

## Slide 9
HISTO UNIT
RAM
Histo – layout (3/4) histo out
fifoHistoPipe1
FifoHistoPipe(0)
(valid)
Idle
others
Occ_sel
4 to 1
valid
Data in
Complete
Data Out
occ
tot
Scan_type
tot
occ
Scan_type
DMA FIFO
Wr_en
Data(max:1)
Data(0)
0
1
Roc
(read-out
completed)
histo

## Slide 10
HISTO UNIT
RAM
Histo – layout (4/4) misc
DMA FIFO
empty
Rd_en
valid
rfr
+1 adder
rst
en
FSM is
RESET
or SAMPLE
or PREPARE
din
out
If localAdd < highAdd
AND
(mod = 0 OR rfr = 1)
THEN -> 1
ELSE -> 0
localAdd

## Slide 11: Sp6fmt Status Register
// Status bits
#define STAT_SIMULATION_BIT 31
#define STAT_EXT_HISTRAM_BIT 30
#define STAT_DMA_RDY_BIT 29
#define STAT_HIST_RFR0_BIT 28
#define STAT_HIST_RFR1_BIT 27
#define STAT_HIST_RFD0_BIT 26
#define STAT_HIST_RFD1_BIT 25
#define STAT_HIST_ROC0_BIT 24
#define STAT_HIST_ROC1_BIT 23
#define STAT_LAST_BIT 23

## Slide 12: Modification implemented into histo unit

## Slide 13
RESET
INIT
SAMPLE
READOUT
PREPARE
CLEAN
IDLE
Select ScanType
Select ReadOut mode
HiAddr <= controlReg
localAdd= MaxAddr and toggle = ‘1’
mode
RamValidPipe=0
And
globFifoEmpty = 1
mode
localAdd = HighAddr and toggle = ‘1’
ramCleanAdd
=HighAddr and toggle = ‘1’
mode
Async rst
T
F
T
T
F
F
1
F
1
1
0
T
0
0
+1 adder
rst
en
Async rst
din
out
State = RESET
Init count
InitCount= MaxCount
T
F

## Slide 14: Histo – layout (1/4) enables and address
Sample
Init
Readout
Clean
others
ramWrHisto
toggle
0
Sample
Readout
others
enable
rfr
AND
toggle
0
ramRd
ramClean
WE
RE
R_ack
Clean
Readout
others
0
ramValidPipe
ramValidPipe1
FifoHistoPipe(0)
(valid)
Sample
others
LocalAdd
PixAddr
Sample
Readout
Clean
others
LocalAdd
HISTO UNIT
RAM
WrAddr
RdAddr
writeAddrHisto
ramCleanAddr
AckAddr

## Slide 15
HISTO UNIT
RAM
Histo – layout (2/4) data
tot
Tot_val
*
+
+
+
1
Sample
others
0
ramDatainHisto
WrData
RdData
ramDataOut
ramDataOutPipe
fifoHistoPipe1
tot
Tot_ack

## Slide 16
HISTO UNIT
RAM
Histo – layout (3/4) histo out
fifoHistoPipe1
FifoHistoPipe(0)
(valid)
ramCleanAddr
= highAddr then 1
Else 0
Occ_sel
4 to 1
valid
Data in
Complete
Data Out
occ
tot
Scan_type
tot
occ
Scan_type
DMA FIFO
Wr_en
Data(max:1)
Data(0)
0
1
Roc
(read-out
completed)
histo

## Slide 17
HISTO UNIT
RAM
Histo – layout (4/4) misc
DMA FIFO
empty
Rd_en
valid
rfr
+1 adder
rst
en
FSM is
RESET
or SAMPLE
or PREPARE
din
out
If localAdd < highAdd
AND
(mod = 0 OR rfr = 1) AND toggle
THEN -> 1
ELSE -> 0
globFifoEmpty
(= AND of empties
Of three fifos in
ssram_interface)
1
toggle

## Slide 18: Ssram_interface layout
HISTO
R_ack
WE
RE
WrAddr
RdAddr
AckAddr
WrData
RdData
tot
Tot_ack
globFifoEmpty
(= AND of empties
Of three fifos
ReadRequest FIFO
we
din
WriteRequest FIFO
we
din
ReadAckFIFO
valid
empty
re
empty
re
scheduler
dout
scheduler
empty re
EFB CLOCK DOMAIN
SRAM CLOCK DOMAIN
din
valid
valid
dout
dout
we
SRAM
CONTROLLER
RdAddr
tot
0
1
WrAddr
Addr
WE_n
DataOut
DataIn
RdAddr + tot

## Slide 19
The scheduler is a simple state machine that read from either fifo A or B
When both are NOT empty it balances the read accesses
(e.g. 4 consecutive for every fifo) in order to minimize bus contention
occurring when read->write or write->read

## Slide 20: Controller layout
Addr
18
Data
32
WE_n
1
CE
Addr
18
Data Out
32
Data In
32
WE_n
1
driven by ramClk ck
driven by ramTxClk ck

## Slide 21
Clock distribution
100 MHz
100 MHz
Ssram1_if
Sram2_if
100 MHz
100 MHz
100 MHz
COMPENSATION = EXTERNAL
CLK_FEEDBACK = CLKOUT0
CLKOUT0
21
100 MHz
100 MHz
COMPENSATION = EXTERNAL
CLK_FEEDBACK = CLKOUT0
CLKOUT0
DCM
SSRAM2
SSRAM1

## Slide 22: Miscellanea
File histoTop_tb simulates histo functionalities stand-alone, writes histo in txt file
Written a mywave.do for viewing with modelsim all histogram->ssram signals
File SimGen.cpp read txt file and compares with emulation
Changes in addrConverter.vhd
  -- old tCol0 <= conv_integer(unsigned(col)) - 1;
  -- old tRow0 <= conv_integer(unsigned(row)) - 1;
  tCol0 <= conv_integer(unsigned(col - '1'));
  tRow0 <= conv_integer(unsigned(row - '1'));
rx_decoder_instance, rx_boc2rod_instance commented out in formatter
3 differents ucf (general + sram1 + sram2)
Bufio, bufio_fb and pll LOCED
Added tig for false path through sram_interface fifos (they were analyzed because two clocks
derive from the 100 MHz input)
Moved constraints of input clocks (both 100 and 40) from _n to _p
  #TIMESPEC TS_CLK100in_N = PERIOD "CLK100in_N" TS_sys_clk_pin PHASE 5 ns HIGH 50%;
  TIMESPEC TS_CLK100in_P = PERIOD "CLK100in_P" TS_sys_clk_pin HIGH 50%;

## Slide 23: Miscellanea (2)
BRAM and SRAM versions are selected by setting Synthesis Option
  –generics useExtRam = true (or useExtRam = false)
No FF placement in IOB! Sram data, addresses and we_n is grouped in UCF and only OFFSET OUT and
  IN are used
Synthesis and Implementation options are default
  (Design Goal and Strategy : Balanced – Xilinx default)
When compiling FW for BRAM comment INST "*rw_tff_p*" IOB = force; in both sram UCFs
  (if not yet commented out)
Address, Data and we_n pins are set to DRIVE = 6 and slew = fast ;
  Clock DRIVE = 8 and slew = fast;
  others DRIVE = 8 and slew = slow;

## Slide 24: Tests in Bologna
Performances confronted with sp6fmt.bit rev 10596
Loaded histClient.elf rev 10596
Tested with IblUtils/iblHistoTest slightly modified by Davide (for the Bologna testbench) and thanks
  to Marcello’s hint (removed IP assigment)